## Slide 1: Virtual Instrumentation
Using non-NI hardware with Labview - LECTURE
Innovative Teaching Approaches in development of Software Designed Instrumentation and its application in real-time systems

## Slide 2
Faculty of Physics
Warsaw University of Technology
Zagreb University of
Applied Sciences
Faculty of Technical
Sciences
Ss. Cyril and Methodius
University
Faculty of Electrical Engineering
and Information Technologies
School of Electrical
Engineering
University of Belgrade
Innovative Teaching Approaches in development of Software Designed Instrumentation and its application in real-time systems

## Slide 3: Arduino
open-source platform
widely used
can be programmed using specialized IDE
low cost
different models
  uno, mega, nano
Inputs & outputs
  depend on the model
  digital IO
    PWM, interrupt, I2C, SPI, etc.
  analog IO

## Slide 4: Raspberry PI
small single-board computer
different generations
  1, 2, 2B, 3, 3B, 4 (latest version)
runs real-time operating system
  Rasbian (linux debian distribution)
low cost
multiple general-purpose input/output pins (GPIO)
  number depends on the model

## Slide 5: Communication with the third-party harware
communication protocol
  between Labview environment and third-party software
  LINX framework
    add-on for Labview
real-time deployment (LINX Application builder)
  Labview runtime on the target device (third-party software)

## Slide 6: Communication protocol
serial
network
  (TCP/IP)
  Bluetooth
  etc..
a lot of programming on the both sides of the communication channel
new application protocol needs to be defined

## Slide 7: Linx Framework
free framework
installation via Package Manager
good set of libraries
ideal for:
    students home projects and learning Labview
    prototyping
Arduino can be used as acquisition device
  not a real-time system
    requires constant connection to the computer running Labview
  limitations when using libraries
    if the library is not working not much to do
  development stopped in 2016

## Slide 8: Real-time deployment (LINX Application builder)
Programming in Labview using LINX framework
running the code on the Raspberry PI without the connection to the computer with the Labview environment
Labview runtime engine is installed on the target device
VI is started on the startup of the target device

## Slide 9: Digital I/O example
VI that reads a digtal input signal (for example a button)
based on the input signal toggle two digital outputs with opposite values (for example a DC motor driver)

## Slide 10: PWM control example
Vi that controls the intensity of the LED connected to the digital pin 3 of the target device.

## Slide 11: Servo motor control example
Control the servo motor connected to the digital pin 9 of the target device

## Slide 12: Analog I/O example
VI that reads analog value from the analog input pin 0 and stores it in an array. VI displays the arithmetic mean of the read values to the user.

## Slide 13: RealTime application on Raspberry PI (1)
requirements are:
  Labview 2014 sp1, 32 bit
  MakerHub add-on for Labview
  Rasbian OS on Raspberry PI
    Raspbian Jessie
Connection tto Raspberry PI
  Serial, network (WiFi, Ethernet cable)
for network communication SSH protocol is used
  it needs to be enabled on the Raspberry

## Slide 14: RealTime application on Raspberry PI (2)
install the Labview runtime on the Raspberry PI
  automatically with the MakerHub add-on
building the application for the target device
deploying the application
runnig the application on the device startup
restarting the target device

## Slide 15
Thanks!
Innovative Teaching Approaches in development of Software Designed Instrumentation and its application in real-time systems