## Slide 1: Signal conditioning and data acquisition
Innovative Teaching Approaches in development of Software Designed Instrumentation and its application in real-time systems
Faculty of Physics
Warsaw University of Technology
Zagreb University of
Applied Sciences
Faculty of Technical
Sciences
Ss. Cyril and Methodius
University
Faculty of Electrical Engineering
and Information Technologies
School of Electrical
Engineering
University of Belgrade

## Slide 2: Outline
Introduction to sensors and data acquisition
  Sensor model
  Analog and digital signals
Signal sources and wiring
  Grounded signal source
  Floating signal source
Coherent interference and suppression
  Electrostatic interference
  Electromagnetic interference
Grounding and shielding
  Serial and parallel grounding
  Guarding and driven shields
Signal sampling
Interfacing DIO applications

## Slide 3: INTRODUCTION TO SENSORS AND CONCEPTS OF DATA ACQUISITION

## Slide 4: INTRODUCTION TO DAQ
What is a data acquisition system?
  Data acquisition is the process by which physical phenomena from the real world are transformed into electrical signals that are measured and converted into a digital format for processing, analyzing, and storage by a computer.
Concepts of data acquisition and test and measurement
  Computer which is used to program test equipment and manipulate or store data
  Data acquisition plug-in boards, external board chassis, or discrete instruments

## Slide 5: Typical data acquisition system
Sensor/transducer
Signal conditioning
Data acquisition hardware (board or measurement system)
Data acquisition software

## Slide 6: WHAT IS A SENSOR?
A sensor is a device that receives a stimulus and responds with an electrical signal.

## Slide 7: SENSOR MODEL
This quantity conversion can be direct or it may require transducers.
Example:
  A chemical sensor may have a part which converts the energy of a chemical reaction into heat (transducer) and another part, a thermopile, which converts heat into an electrical signal.

## Slide 8: SENSOR’S RESPONCE
Sensors produce output signal in a form of:
  Voltage
  Current
  Charge
The voltage, current or charge may be describe by:
  Amplitude
  Frequency
  Phase
  Duty cycle
  Digital code

## Slide 9: SIGNAL TYPES
SIGNAL
ANALOG
Continuous
Infinite range of values
DIGITAL
Discrete
Finite range of values

## Slide 10: ANALOG SIGNALS
Parameters
  Level
  Shape
  Phase
  Period
  Frequency

## Slide 11: DIGITAL SIGNALS
Parameters
  State
  Frequency
  Period
  Duty cycle

## Slide 12: SIGNAL SOURCES AND WIRING

## Slide 13: TYPES OF SIGNAL SOURCES
GROUNDED
One of the signal source terminals is connected to ground
FLOATING
None of the signal source terminals is connected to ground

## Slide 14: MEASURING GROUNDED SIGNAL SOURCES
Ground-referenced measurement

## Slide 15: MEASURING GROUNDED SIGNAL SOURCES
Differential measurement

## Slide 16: MEASURING FLOATING SIGNAL SOURCES
Ground referenced and differential measurement

## Slide 17: Normal Mode and Common Mode Voltages
Normal mode voltage VNM
Common mode voltage VCM

## Slide 18: GROUND LOOPS
Degradation of measurements due to ground loops

## Slide 19: Bipolar vs. Unipolar AND SINGLE ENDED VS. DIFFERENTIAL
Differential configuration results in better noise immunity
Practical experiment to test the single ended vs. differential input noise immunity:

## Slide 20: NOISE INTERFERENCE

## Slide 21: SOURCES OF NOISE INTERFERENCE
Inherent noise
Interference (transmitted) noise

## Slide 22: TRANSMITTED NOISE
Additive
Multiplicative

## Slide 23: CAPACITIVE AND INDUCTIVE COUPLING

## Slide 24: SIEBECK NOISE

## Slide 25: GROUNDING AND SHILDING (NOISE SUPRESSION)

## Slide 26: SIGNAL GROUNDING
What is “ground”?
Types of signal grounding:
  Singe point ground systems
  Multi point ground systems
  Hybrid grounding systems

## Slide 27: Single point grounding
Series connection
Parallel connection

## Slide 28: MULTI POINT GROUNDING

## Slide 29: HYBRID GROUNDS
Acts like a single-point ground at low frequencies and a multi-point ground at high frequencies
Acts like a single-point ground at high frequencies and a multi-point ground at low frequencies

## Slide 30: SHIELDING
What is the purpose of shielding?
Types of shields:
  Electric shielding
  Magnetic shielding

## Slide 31: ELECTRIC SHIELDING
Practical rules:
Electrostatic shield should be connected to the reference potential the circuit (Fig. a)
If a shielding cable is used, its shield must be connected to the signal referenced node at the signal source side (Fig. a)
Shield for each segment must be tied to the other segments (if any) (Fig. b)
A shielded cable must never be grounded at both ends
The cable shield must be connected to the box (Fig. c)
Use short leads

## Slide 32: MAGNETIC SHIELDING
Practical rules:
Locate the receiving circuit as far as possible from the source of the magnetic field
Avoid placing wires parallel to the magnetic field
Use a twisted pair of wires for conductors carrying the high-level current
Shield the magnetic field with an appropriate material for the frequency and strength.

## Slide 33: INERFACING ANALOG AND DIGITAL SIGNALS

## Slide 34: ANALOG TO DIGITAL CONVERSION
Sampling
Quantization
Coding

## Slide 35: SIGNAL SPECTRUM PRIOR AND AFTER SAMPLING

## Slide 36: ALIASING

## Slide 37: INTERFACING MECHANICAL SWITCHING
Contact bouncing
Hardware de-bouncing circuit

## Slide 38: DIGITAL ISOLATION
Input
Output

## Slide 39
Innovative Teaching Approaches in development of Software Designed Instrumentation and its application in real-time systems
ITASDI
Co-funded by the
Erasmus+ Programme
of the European Union