## Slide 1: Data Acquisition Techniques Using LabVIEW
Innovative Teaching Approaches in development of Software Designed Instrumentation and its application in real-time systems
Faculty of Physics
Warsaw University of Technology
Zagreb University of
Applied Sciences
Faculty of Technical
Sciences
Ss. Cyril and Methodius
University
Faculty of Electrical Engineering
and Information Technologies
School of Electrical
Engineering
University of Belgrade

## Slide 2: Outline
Data Acquisition Systems Overview
Overview of NI-DAQmx VIs
Analog Input Acquisition Techniques
  Single Sample Software-Timed Acquisition
  Finite Buffered Acquisition
  Continuous Buffered Acquisition
Analog Output Acquisition Techniques
  Single Sample Generation
  Finite Buffered Generation
  Continuous Buffered Generation
Digital Input / Output Acquisition Techniques
  Hardware-Timed Digital Input / Output

## Slide 3: DATA ACQUISITION SYSTEMS OVERVIEW

## Slide 4: What is Data Acquisition?
Data acquisition – DAQ
Automatic collection of data from sensors, instruments and devices
Measuring a physical phenomenon (e.g. light, temperature, pressure, sound…)

## Slide 5: DAQ System Overview
Signal Conditioning
Sensor/ Signal
I/O
DAQ Hardware
Bus
DAQ Software
DAQ system building blocks
  Sensor/signal
  DAQ hardware
  Signal conditioning
  DAQ software

## Slide 6: Sensors
Converting physical phenomena into data the computer can use
Sensors (transducers) convert physical phenomena into an electrical signal
Different sensor types have different requirements
Phenomena | Sensors
Temperature | Thermocouples Resistive temperature detectors (RTDs) Thermistors Integrated circuit sensors
Light | Vacuum tube photosensors Photoconductive cells
Sound | Microphones
Force and pressure | Strain gage Piezoelectric transducers Load cells
Position (displacement) | Potentiometers Linear voltage differential transformers (LVDTs) Optical encoders
Fluid flow | Head meters Rotational flowmeters Ultrasonic flowmeters
pH | pH electrodes

## Slide 7: Signals
Signals in terms of data acquisition
Types of signals:
  Analog
  Digital
Types of information to be obtained from signals:
  State
  Rate
  Level
  Shape
  Frequency etc.

## Slide 8: Signals – Analog Signals
Analog signals can be at any voltage level with respect to time
Different physical aspects to be measured compared to digital signals
Analog signal information:
  Level
  Shape
  Frequency

## Slide 9: Analog Input - Signal Sampling
Analog signals are converted to digital form before being processed by a computer
Finite set of values in the independent (time/space) and dependent (amplitude) variable
Converting analog signal into a digital representation is done by using an analog-to-digital (A/D) converter

## Slide 10: Signals – Digital Signals
Digital signals have only two possible states – ON (logic high) or OFF (logic low)
Only two aspects of digital signals can be measured:
  State
  Rate

## Slide 11: Signal Conditioning
Signal conditioning is the process of measuring and manipulating signals to improve the accuracy, isolation and filtering of signals during acquisition
The purpose of signal conditioning is to take a signal that is difficult for the DAQ device to measure and alter the signal to make it easier to measure.
This may include e.g. signal amplification, noise filtering, compensation or applying excitation current

## Slide 12: DAQ Hardware
Components of a typical DAQ system:
  1 – Signal
  2 – Terminal Block
  3 – Cable
  4 – DAQ Device
  5 – Computer

## Slide 13: DAQ Hardware – DAQ Devices
Interfaces
  1. Computer I/O Interface Circuitry
  2. I/O connector
  3. Real-time system integration (RTSI) bus

## Slide 14: DAQ Software
The final component of a complete DAQ system is the software
Typical DAQ software includes drivers and application software
LabVIEW
NI-DAQmx

## Slide 15: Overview of NI-DAQmx VIs

## Slide 16: NI-DAQmx VIs

## Slide 17: Waveform Data Type
The wave form data type is a cluster that consists of the following elements:
  Y
  t0
  Attributes
Benefits of using the waveform data type:
  Presence of t0
  Easier graphing
  Easier multiple plot graphing

## Slide 18: ANALOG INPUT ACQUISITION TECHNIQUES

## Slide 19: Using the DAQmx Analog Read VI

## Slide 20: Single Sample Software-Timed Acquisition

## Slide 21: Finite Buffered Acquisition

## Slide 22: Finite Buffered Acquisition

## Slide 23: Continuous Buffered Acquisition

## Slide 24: Continuous Buffered Acquisition

## Slide 25: ANALOG OUTPUT ACQUISITION TECHNIQUES

## Slide 26: Using the DAQmx Analog Write VI

## Slide 27: Single Sample Generation
Software-timed
Hardware-timed
Setting the timing for an analog output generation
  Sample clock
  On demand
  Use waveform

## Slide 28: Finite Buffered Generation

## Slide 29: Finite Buffered Generation – Sample Clock

## Slide 30: Finite Buffered Generation – Use Waveform

## Slide 31: Continuous Buffered Generation

## Slide 32: Continuous Buffered Generation

## Slide 33: DIGITAL Input / Output ACQUISITION TECHNIQUES

## Slide 34: Digital I/O Overview
TTL signals
Digital Terminology
  Bit
  Byte
  Line
  Port
  Port width
  Mask
Digital Channel Data Formats
  Line format (Boolean)
  Port format (Integer)

## Slide 35: Using the DAQmx Digital Read and Write VI

## Slide 36: Hardware-Timed Digital I/O – Onboard SampleClock

## Slide 37: Hardware-Timed Digital I/O – Correlated Digital I/O

## Slide 38
Innovative Teaching Approaches in development of Software Designed Instrumentation and its application in real-time systems
ITASDI
Co-funded by the
Erasmus+ Programme
of the European Union