## Slide 1: Virtual Networks: SDN and NFV
Innovative Teaching Approaches in development of Software Designed Instrumentation and its application in real-time systems
Faculty of Physics
Warsaw University of Technology
Zagreb University of
Applied Sciences
Faculty of Technical
Sciences
Ss. Cyril and Methodius
University
Faculty of Electrical Engineering
and Information Technologies
School of Electrical
Engineering
University of Belgrade

## Slide 2: Contents
Introduction
SDN
  SDN Architecture
  SDN Objectives
  SDN Capabilities
  SDN OpenFlow
  SDN Security
NFV
  NFV Achitecture
  NFV Benefits
  Relationship between NFV and SDN
Conclusion

## Slide 3: Introduction
Network virtualization (NV) is the process of combining hardware and software network resources and network functionality into a single, software-based administrative entity, named virtual network framework.
NV=SDN+NFV
The trend beyond software-defined instrumentation is giving engineers unprecedented control over automated test systems and enabling new types of applications.

## Slide 4: The Big Picture
Notes: Network Functions Virtualisation aligns closely with the SDN objectives to use commodity servers and switches

## Slide 5: SDN introduction
Software-Defined Networking is an emerging network architecture which decouples the network control and forwarding functions enabling the network control to become directly programmable and the underlying infrastructure to be abstracted for applications and network services.
Centralizes command and control in the network
Separates the Control plane from the Data plane and Management plane
Although SDN is a relatively new area, it has attracted much attentions from academia, business and industry.

## Slide 6: SDN Architecture
Software-Defined Networking is an Architecture

## Slide 7: SDN Concept by ITU [Rec. Y.3300]
SDN relocates the control of network resources to a dedicated network element, namely SDN controller, which provides a means to program, orchestrate, control and manage the network resources through software.

## Slide 8: SDN Functional architecture
Overview of the SDN functional architecture organized by means of the SDN layering framework [ITU-T Rec. ITU-T Y.3302 (01/2017)]
Notes: Well-defined programming interface between
control- and data planes.
-Applications running on controller manage and
control underlying data plane

## Slide 9: SDN Objectives
The objectives of SDN are to realize:
  Faster network business cycles; SDN reduces the response time of business requests to network providers
  Acceleration of innovation: SDN accelerates business and/or technical innovation through more flexibility of the network operations, thus making trials easier;
  Accelerated adaptation to customer demands: SDN facilitates the accommodation of customer's connectivity requirements by means of dynamic negotiation of network service characteristics and of dynamic network resource control;

## Slide 10: SDN Objectives (2)
The objectives of SDN are to realize:
  Improved resource availability and usage efficiency: SDN is meant to improve network resource availability and efficiency, in particular when combined with network virtualization, due to the introduction of a high level of automation in the overall service delivery and operation procedures, from service parameter negotiation to fulfilment and assurance;
  Customization of network resources including service-aware networking: SDN allows network customization for the network services which have different requirements, through the programming of network resource operations, including the dynamic enforcement of a set of policies (QoS).

## Slide 11: Unified SDN overview
MAN Network
Access
Data Center
BRAS
pCPE
Virtualization
vCPE
vBRAS
vPE Router
vFW
vLB
E2E Unified SDN/NFV Service Orchestrator
GW
OpenStack
（DC controller）
TOR
Legacy
Domain A
DomainB
Vender specific
ONOS
ODL
SDN Controller

## Slide 12: SDN High-level capabilities
SDN provides the following high-level capabilities:
  Programmability: The behavior of network resources can be customized by SDN applications through a standardized programming interface for network control and management functionality. The user of the interface may be network providers, service providers, and customers including end-users. This enables the SDN applications to automate the operations of network resources according to their needs.
  Resource abstraction: The property and behavior of underlying network resources can be appropriately abstracted and understood, orchestrated, controlled and/or managed by those who program them, thanks to relevant, standard information and data models. These models provide a detailed, abstracted view of physical or virtualized network resources.

## Slide 13: Software defined networking functional capabilities
SDN Controller
DPI
Transparent
Caching
MSP
Services
Chaining
Service creation
Intelligent steering
Dynamic offload
Subscriber personalization
Virtual
Networks
vBNG
vPE
vEPG
Telco Cloud enabler
Network automation
Scaling & load sharing
WAN VPN interconnect
Multi-Layer
Transport
Control
Forward
Forward
Cost & Efficiency
Service abstraction
VPN automation
Application aware TE
ML optimization
Switch
XC
Router
OF Switch
ROADM
Transponder
vEGW
vHGW

## Slide 14: SDN Controller overview
Most carriers’ network is hybrid network which includes legacy and SDN, and virtual network.
SDN controller focus on network resource abstraction and path calculation
SDN controllers serve as a type of operating system for network.
SDN orchestration focus on end to end service and resource orchestration and it is key to enable agile service across multi-domain，multi-layer and multi-vendor.
Legacy
Domain
SDN Domain A
SDN Domain B
Controller
(ONOS)
EMS
APP/OSS/BSS
SDN Orchestrator
Controller (ODL)

## Slide 15: SDN OpenFlow controller
Currently OpenFlow is the most popular SDN protocol/standard and has a set of design specifications.
As a standard SDN protocol, OpenFlow was proposed by Stanford.
Regarding testbeds of OpenFlow, many designs have been proposed.
They use open source codes to control universal SDN controllers and switches.
Notes: OpenVSwitch (OVS)

## Slide 16: SDN OpenFlow controller extension
In its current version, OpenFlow is not able to configure QoS parameters in a dynamic and on-demand manner (i.e., only manually).
In order to deal with QoS problems in dynamic approach, a framework called QoSFlow that enables QoS management in OpenFlow environment.*
QoSFlow is an extension of the standard OpenFlow controller which provides multimedia delivery with QoS.
* Airton Ishimori, Fernando Farias, Igor Furtado, Eduardo Cerqueira, Antnio Abelm, “Automatic QoS Management on OpenFlow Software-Dened Networks” in downloadable from: http://siti.ulusofona.pt/aigaion/index.php/attachments/single/362. 2012
Notes: QoSFlow modules

## Slide 17: SDN QoS controller Architecture
Controller Architecture for QoS Optimization
The controller has powerful capabilities to specify QoS requirements. It can also directly control the flow table in order to differentiate between different priorities of traffic.
The communications between the controller and the switches may be secured by some standards such as SSL.
Source: H. E. Egilmez, B. Gorkemli, A. M. Tekalp, and S. Civanlar, “Scalable video streaming over OpenFlow networks: an optimization framework for QoS routing,” in Proc. of IEEE Int. Conf. on Image Processing, 2011, pp. 2241-2244.
Notes: Note that the forward layer has to implement the policing
functions in order to ensure that the clients obey the Service
Level Agreements (SLAs) specified in their QoS contracts.

## Slide 18: SDN QoS controller Architecture (2)
In the SDN Controller Architecture for QoS Optimization, the following three extra features should exist:
  Resource monitoring: The forwarders should comprehensively monitor their available network resources and report periodically to the controller. The controller may poll the forwarder for such profile.
  Resource signaling: Each forwarder should use signaling messages to communicate with the controller on the current resource consumption so that certain actions can be taken by the controller, such as updating the flow table, changing QoS parameters, etc.
  Resource reservation: From time to time the controller may command a forwarder to reserve certain resources for future QoS needs.
This includes the reservation of buffer size, memory space, CPU calculation time, and other resource requirements.

## Slide 19: OpenFlow model
OpenFlow is flow-oriented protocol and has switches and ports abstraction to control the flow.
The controller communicates with the OpenFlow switch and manages the switch through the OpenFlow protocol.
An OpenFlow switch can have multiple flow tables, a group table, and an OpenFlow channel.
* Single-point controller can manage all flow tables in different switches!
Notes: Single control also has single-point failure issue. To solve the above issue, we can use
distributed controllers in different locations.

## Slide 20: OpenFlow Architecture components
The OpenFlow architecture typically includes 3 important components:
  1) Switches: OpenFlow defines an open source protocol to monitor/change the flow tables in different switches and routers. An OpenFlow switch has at least three components: a) flow table(s), each with an action field associated with each flow entry, b) a communication channel, which provides link for the transmission of commands and packets between a controller and the switch, c) the OpenFlow protocol, which enables an OpenFlow controller able to communicate with any router/switch.

## Slide 21: OpenFlow Architecture components (2)
The OpenFlow architecture typically includes 3 important components:
  2) Controllers: A controller can update (revise, add, or delete) flow-entries from the flow table on behalf of the users experiments. A static (versus dynamic) controller can be a simple software unit running on a computer to statically (versus dynamically) establish packet path between a group of hosts.
  3) Flow-entries: Each flow-entry includes at least a simple action (network operation) for that flow item.
Most OpenFlow switches support the following three actions: (a) sending this flow’s packets to a port, (b) encapsulating this flows packets and sending to a controller, and (c) dropping this flows packets.

## Slide 22: OpenFlow actions and versions
Most OpenFlow switches support the following three actions:
  (a) sending this flow’s packets to a port, (b) encapsulating this flows packets and sending to a controller, and (c) dropping this flows packets.
OpenFlow has gone through many standard iterations, an it is currently on version 1.5.1; however only version 1.0 is available for practical software and hardware design.
Moreover, version 1.6 has been available since September 2016, but accessible only to ONF's members

## Slide 23: OpenFlow 1.0 Header and Flow Table with Fields

## Slide 24: OpenFlow Table entries
Each OpenFlow Table entry has two timers:
  idle_timeout: seconds of no matching packets after which the flow is removed zero means never times-out.
  hard_timeout: seconds of no matching packets after which the flow is removed zero means never times-out.
If both idle_timeout and hard_timeout are set, then the flow is removed when the first of the two expires.

## Slide 25: Packet flow through the processing pipeline
Source: https://www.opennetworking.org/wp-content/uploads/2014/10/openflow-spec-v1.4.0.pdf

## Slide 26: Beyond OpenFlow – Other SDN protocols
Besides OpenFlow (the most popular SDN protocol), there exist other SDN implementations.
For instance, IEEE P1520 standards* have defined Programmable Network Interfaces. It can be seen as an initial model of SDN, since it also has network programming abstractions.
ForCES (Forwarding and Control Element Separation)** is another standard defined by IETF.
* Biswas, A. A. Lazar, J. F. Huard, K. S. Lim, S. Mahjoub, L. F. Pau, M. Suzuki, S. Torstensson, W. Wang, and S. Weinstein, “The IEEE P1520 Standards Initiative for Programmable Network Interfaces,” IEEE Commun. Mag.,Vol. 36, no. 10, 1998, pp. 6470.
** A. Doria, J. H. Salim, R. Haas, H. Khosravi, W. Wang, L. Dong, R. Gopal, and J. Halpern, “Forwarding and Control Element Separation (ForCES) Protocol Specification,” in [Online]. Available: http://tools.ietf.org/html/rfc5810

## Slide 27: SDN Security
Software-defined networking (SDN) enables the administrators to configure network resources very quickly and to adjust network-wide traffic flow to meet changing needs dynamically.
One of the most important challenges is SDN security.
SDN applications can be seen as the "SDN network brains", since they implement a majority of network functionalities.
So, attacks on SDN applications if not stopped early enough, can impact the SDN control layer.

## Slide 28: SDN Security (2)
Security reference
architecture for SDN
[Rec. ITU-T X.1038 (10/2016)]

## Slide 29: SDN Security (3)
SDN security requirements mapping to security threats. More details: [Rec. ITU-T X.1038 (10/2016)]

## Slide 30: SDN Security (4)
SDN security requirements mapping to security threats. More details: [Rec. ITU-T X.1038 (10/2016)]

## Slide 31: SDN Simulators
Pareto Optimal Controller Placement (POCO) Matlab-based tool:
  https://github.com/lsinfo3/poco
OpenDaylight SDN Controller with the Mininet Network Emulator:
  https://www.opendaylight.org/platform-overview-beryllium
Mininet Network Emulator:
  http://mininet.org/
NS-3 Network Simulator: https://www.nsnam.org/
Opensource Openflow network emulation (OFNet)
  http://sdninsights.org/
Notes: https://www.researchgate.net/post/What_is_the_best_simulator_emulator_for_SDN

## Slide 32: SDN Simulators (2)
EstiNet 9.0 OpenFlow Network Simulator:
  http://www.estinet.com/
CloudSimSDN *
* J. Son, A. V. Dastjerdi, R. N. Calheiros, X. Ji, Y. Yoon and R. Buyya, "CloudSimSDN: Modeling and Simulation of Software-Defined Cloud Data Centers," 2015 15th IEEE/ACM International Symposium on Cluster, Cloud and Grid Computing, Shenzhen, 2015, pp. 475-484.
Notes: https://www.researchgate.net/post/What_is_the_best_simulator_emulator_for_SDN

## Slide 33: NFV Introduction
Network Function Virtualization (NFV) is implementing network functions in software - that run today on proprietary hardware - leveraging (high volume) standard servers and ICT virtualization
Supports multi-versioning and multi-tenancy of network functions.
Allows use of a single physical platform for different applications, users and platforms
Enables new ways to implement resilience, service assurance, test, diagnostics and security surveillance
Facilitates innovation towards new network functions and services that are only practical in a pure software network environment

## Slide 34: NFV Introduction (2)
As an emerging technology, NFV brings several challenges to network operators, such as the guarantee of network performance for virtual appliances, their dynamic instantiation and migration, and their efficient placement.
While SDN is typically thought of as managing and automating tasks for physical devices, NFV is all about provisioning new networking devices.
  SDN may then be used to manage the new virtual as well as the existing physical devices.
Notes: How is NFV Different from SDN,
Rethinking relayering

## Slide 35: NFV: One Vision
Classical Network Appliance Approach
BRAS
Firewall
DPI
CDN
Tester/QoE
monitor
WAN
Acceleration
Message
Router
Radio/Fixed Access
Network Nodes
Carrier Grade NAT
Session Border
Controller
PE Router
SGSN/GGSN
Fragmented, purpose-built hardware.
Physical install per appliance per site.
Hardware development large barrier to entry for new vendors, constraining innovation & competition.
Network Functions Virtualisation Approach
High volume Ethernet switches
High volume standard servers
High volume standard storage
Orchestrated,
automatic & remote install.
Competitive &
Innovative
Open Ecosystem
Independent
Software Vendors

## Slide 36: Defining NFV
NFV transforms how network operators architect their infrastructure by leveraging the full-blown virtualization technology to separate software instance from hardware platform, and by decoupling functionality from location for faster networking service provisioning.

## Slide 37: Benefits of NFV
Flexibility to easily, rapidly dynamically provision and instantiate new services in various locations (i.e. no need for new equipment install).
Reduced time-to-market by minimizing the typical network operator cycle of innovation. More service differentiation and customization.
Improved operational efficiency by taking advantage of the higher uniformity of the physical network platform and its homogeneity to other support platforms.

## Slide 38: Benefits of NFV (2)
Reduced equipment costs through equipment consolidation on high volume industry standard servers leveraging the economies of scale of the IT industry.
Reduced operational costs: reduced power, reduced space, improved network monitoring.
Software-oriented innovation (including Open Source) to rapidly prototype and test new services and generate new revenue streams.
IT-oriented skillset and talent (readily available in global geography, flexible).

## Slide 39: NFV - ETSI Reference Architecture
* ETSI, “Network Functions Virtualisation (NFV); Architectural Framework,” GS NFV 002 (v. 1.1.1), Oct. 2013.
Notes: Operation/business support systems ----------- =====Shared Hardware resources

## Slide 40: NFV Architecture

## Slide 41: NFV major differences
NFV introduces the following three major differences:
  Separation of software from hardware: This separation enables the software to evolve independent from the hardware, and vice versa.
  Flexible deployment of network functions: NFV can automatically deploy network function software on a pool of hardware resources that may run different functions at different times in different data centers.
  Dynamic service provisioning: Network operators can scale the NFV performance dynamically and on a grow-as-you-need basis with fine granularity control based on the current network conditions.

## Slide 42: Baseline NFV Architecture
NFV Applications Domain
NFV Container Interface

## Slide 43
Relationship between NFV and SDN
NFV deploys virtual network equipment
SDN traditionally manages physical network equipment and software.
SDN can refer to managing both physical and virtual equipment and environment

## Slide 44: Illustration of SDN vs NFV

## Slide 45: NFV Use Cases
Here, we describe two use cases of NFV:
  the virtualization of a mobile core network and a home network.
The virtualization of a mobile core netwok (EPC) targets the mobility management entity (MME), home subscriber server (HSS), SGW, PGW, and policy and charging rules function (PCRF).
  The virtualization of EPC for 4G LTE networks and its coexistence with the legacy EPC is done.
  The coexistence is made possible through technologies such as MME pooling. We note that it is possible to virtualize only part of the mobile core network, such as SGW and PGW, and use physical appliances for other components.

## Slide 46: NFV Use Cases (2)
Virtualization of EPC and its coexistence with legacy EPC

## Slide 47: NFV Use Cases (3)
Benefits from NFV in EPC:
  By virtualizing the aforementioned network functions, Cloud EPC allows us to move toward a more intelligent, resilient, and scalable core architecture.
  NFV enables flexible distribution of hardware resources to eliminate performance bottlenecks and rapid launch of innovative services to generate new revenue sources (e.g., machine-to-machine, M2M, communications).
Challenges: One of the challenging issues of Cloud EPC is that carriers need to dynamically redirect user traffic when scaling offered services.

## Slide 48: NFV Use Cases (4)
NFV in Home Network:
  The architecture of virtualized home networks is given below. The virtualization targets are STBs and a range of components of Residential Gateways, such as firewall, DHCP server, VPN gateway, and NAT router.

## Slide 49: NFV Use Cases (5)
Benefits from NFV in Home Network:
  It reduces the operating expense by avoiding the constant maintenance and updating of the CPE devices, and alleviating the call center and product return burdens.
  It improves the quality of experience by offering near unlimited storage capacity and enabling access to all services and shared content from different locations and multiple devices.
  It allows dynamic service quality management and controlled sharing among user application streams which helps content providers programmatically provision capacity to end users via open APIs.
  It introduces new services more smoothly and less cumbersome by minimizing the dependency on the CPE functions.

## Slide 50: NFV Use Cases (6)
Challenges from NFV in Home Network:
  A fundamental issue in this area is the performance of virtualized packet processing on standard high volume servers. To achieve the same or comparable performance in a virtual environment as in bare metal, we need to carefully design the software architecture and configure the system parameters correctly.
  Finally, security and privacy issue will be another research challenge when sharing virtualized resource among customers to minimize operating cost.

## Slide 51: 5G + NV (NFV & SDN)
Source: View on 5G Architecture - 5G PPP Architecture Working Group (2016)

## Slide 52: Flexibility with NFV+SDN
Source: http://www.itc26.org/fileadmin/ITC26_files/ITC26-Tutorial-Rostami.pdf

## Slide 53: Conclusion
It is envisioned that NFV + SDN, along with cloud computing, will become a critical enabling technology to radically revolutionize the way network operators architect and monetize their infrastructure.
SDN= centralizes and automates management of network devices.
SDNs allow the data and control planes to be separated, and hence to be easier for improvements and management.
NFV is prospectively the unifying revolution among the three, offering more revenue opportunities in the services value chain.
One of the significant cutterpillar of 5G.

## Slide 54
Innovative Teaching Approaches in development of Software Designed Instrumentation and its application in real-time systems
ITASDI
Co-funded by the
Erasmus+ Programme
of the European Union